## Slide 1
SLICC Concept
Example
T1
T2
T3
Instruction Stalls in OLTP?
Many concurrent Transactions
Instruction Caches are Thrashed
Ingredients & Implementation
When to migrate?
Detect – Cache Full
Counting the number of misses incurred by the cache.
Detect – New Segment
Track miss dilution by counting the number of misses within a window of N cache accesses.
Where to go?
Predict where is the next code segment?
Find which other core holds all N cache blocks missed recently.
SLICC: Self-Assembly of Instruction Cache Collectives
for OLTP Workloads
Islam Atta1, Pınar Tözün2, Anastasia Ailamaki2, Andreas Moshovos1
1University of Toronto, 2École Polytechnique Fédérale de Lausanne
Methodology
Zesto: x86 CMP simulator
Shore-MT: storage manager
QEMU Extension
Exploit CMP Integration and OLTP Behavior
CMP Integration
OLTP Behavior
Lots of code reuse
Higher overlap across same-type transactions
Key Results
Effect on Misses
OLTP:
Instruction misses: 58%
Data misses: 7%
Robust:
MapReduce, a non-OLTP workload with a small instruction footprint, is not affected.
Performance
Baseline: no effort to reduce instruction misses
  TPC-C: +60% TPC-E: +79%
Next-line: always prefetch the next-line
  TPC-C: +35% TPC-E: +52%
Upper bound for Proactive Instruction Fetch [Ferdman, MICRO’11]
  TPC-C: ±2%, TPC-E: +21%
  SLICC requires <1KB of storage, while PIF requires ~40KB.
  PIF is a general technique, while SLICC is tailored to workloads with behavior similar to OLTP.
fits in
aggregate L1-I capacity
of a CMP
A transaction's
Instruction footprint
Chart: Instruction Space
| Global | Per Transaction | Global | Per Transaction | TPC-C | TPC-E
Single | 2233 | 9521 | 3454 | 6408.4286
Few | 6931840 | 62243 | 13808068 | 163291.1429
Most | 32264594 | 4691358 | 105929738 | 19671461
Transactions
Execution Flow
T2
T1
T3
T2
T3
T1
T2
T1
T1
T1
T2
T1
T2
T3
T1
T2
T3
0
1
2
3
CORES
T3
Conventional
L1-I
Time
T1
T1
0
1
2
3
CORES
SLICC
T1
T2
T3
T2
T1
T3
T2
T3
T1
T1
Cache Filled 10 times
Cache Filled 4 times
3
1
2
L1-I size
Footprint
Chart: MPKI
| Base | SLICC | SLICC-SW |  | Base | SLICC | SLICC-SW |  | Base | SLICC | SLICC-SW | TPC-C-10 |  | TPC-E |  | MapReduce
I-MPKI | 39.9829 | 25.843 | 17.5589 | 32.0774 | 17.1856 | 12.4782 | 5.81 | 5.8317 | 5.8317
D-MPKI | 32.6111 | 33.8937 | 32.9544 | 30.9176 | 33.2632 | 31.8984 | 1 | 0.9957 | 0.9957
Chart: Speedup over Baseline
| TPC-C-1 | TPC-C-10 | TPC-E | MapReduce
Next-Line | 1.192 | 1.185 | 1.173 | 0.99
PIF-No Overhead | 1.6392 | 1.5889 | 1.4705 | 1.03
SLICC | 1.4501 | 1.4626 | 1.5972 | 1.0056
SLICC-SW | 1.604 | 1.6135 | 1.79 | 1.0056
Better
Target:
Improve Performance for OLTP workloads
How?
Reduce Instruction Misses / Stalls
Why we care?
Online Transaction Processing (OLTP)
  $100 billion/year, +10% annually
    Drives innovation for HW and DB vendors
L1-I size
Footprint
Each
Email: iatta@eecg.toronto.edu
Phone: 416-805-8790
Website: http://islamatta.com
Divided we Fail
United we Succeed
Better