## Slide 1: SLICC Self-Assembly of Instruction Cache Collectives for OLTP Workloads
Pınar Tözün
Anastasia Ailamaki
Islam Atta
Andreas Moshovos

## Slide 2: Online Transaction Processing (OLTP)
$100 Billion/Yr, +10% annually
  E.g., banking, online purchases, stock market…
Benchmarking
  Transaction Processing Council
    TPC-C: Wholesale retailer
    TPC-E: Brokerage market
OLTP drives innovation for HW and DB vendors

## Slide 3: Transactions Suffer from Instruction Misses
Many concurrent transactions
L1-I
size
Footprint
Each
Time
Instruction Stalls due to L1 Instruction Cache Thrashing

## Slide 4: Even on a CMP all Transactions Suffer
Cores
L1-1 Caches
Transactions
All caches thrashed with similar code blocks
Time

## Slide 5: Opportunity
Footprint over Multiple Cores  Reduced Instruction Misses
Technology:
    CMP’s aggregate L1 instruction cache capacity is large enough
Application Behavior:
    Instruction overlap within and across transactions
Multiple L1-I caches
Multiple threads
Time

## Slide 6: SLICC Overview
Dynamic Hardware Solution
How to divide a transaction
When to move
Where to go
Performance
    Reduces instruction misses by 44% (TPC-C), 68% (TPC-E)
    Performance improves by 60% (TPC-C), 79% (TPC-E)
Robust:
non-OLTP workload remains unaffected

## Slide 7: Talk Roadmap
Intra/Inter-thread instruction locality is high
SLICC Concept
SLICC Ingredients
Results
Summary

## Slide 8: OLTP Facts
Many concurrent transactions
Few DB operations
    28 – 65KB
Few transaction types
    TPC-C: 5, TPC-E: 12
Transactions fit in 128-512KB
Overlap within and across different transactions
R()
U()
I()
D()
IT()
ITP()
Payment
New Order
CMPs’ aggregate L1-I cache is large enough

## Slide 9: Instruction Commonality Across Transactions
Lots of code reuse
More Yellow
Even higher across same-type transactions
Most
Few
Single
Chart: 
| Single | Few | Most
All | 2233 | 6931840 | 32264594
Few | 6931840
Most | 32264594
Chart: 
| Single | Few | Most
All | 3454 | 13808068 | 105929738
Few | 6931840
Most | 32264594
TPC-C
TPC-E
All Threads
Chart: 
| Single | Few | Most
Per Transaction Type | 9521 | 62243 | 4691358
Few | 6931840
Most | 32264594
Chart: 
| Single | Few | Most
Per Transaction Type | 6408.4286 | 163291.1429 | 19671461
Few | 6931840
Most | 32264594
Per Transaction
Type
More Reuse

## Slide 10: Requirements
Enable usage of aggregate L1-I capacity
    Large cache size without increased latency
Exploit instruction commonality
    Localizes common transaction instructions
Dynamic
      Independent of footprint size or cache configuration

## Slide 11: Talk Roadmap
Intra/Inter-thread instruction locality is high
SLICC Concept
SLICC Ingredients
Results
Summary

## Slide 12: Example for Concurrent Transactions
T1
T2
T3
Code segments that can fit into L1-I
Transactions
Control Flow
Graph

## Slide 13: Scheduling Threads
T1
T2
T1
T1
T3
T2
T3
T1
T1
T1
T2
T2
T3
T1
T3
0
1
2
3
CORES
T3
Conventional
L1-I
T1
T2
T3
Threads
Time
T1
T1
0
1
2
3
CORES
SLICC
T1
T2
T3
T2
T1
T3
T3
T1
T1
Cache Filled 10 times
Cache Filled 4 times
T2
T2
T2

## Slide 14: Talk Roadmap
Intra/Inter-thread instruction locality is high
SLICC Concept
SLICC Ingredients
Results
Summary

## Slide 15: Migration Ingredients
When to migrate?
Step 1:
Detect: cache full
Step 2:
Detect: new code segment
Where to go?
Step 3:
Predict where is the next code segment?

## Slide 16: Migration Ingredients
Time
Idle cores
When to migrate?
Step 1:
Detect: cache full
Step 2:
Detect: new segment
Where to go?
Step 3:
Where is the next segment?
Loops
Idle
Return back
T1

## Slide 17: Migration Ingredients
When to migrate?
Step 1:
Detect: cache full
Step 2:
Detect: new segment
Where to go?
Step 3:
Where is the next segment?
Time
T2

## Slide 18: Implementation
When to migrate?
Step 1:
Detect: cache full
Step 2:
Detect: new segment
Where to go?
Step 3:
Where is the next segment?
Find signature blocks on remote cores
Miss Counter
Miss Dilution

## Slide 19: Boosting Effectiveness
More overlap across transactions of the same-type
SLICC: Transaction Type-oblivious
Transaction Type-aware
    SLICC-Pp: Pre-processing to detect similar transactions
    SLICC-SW : Software provides information

## Slide 20: Talk Roadmap
Intra/Inter-thread instruction locality is high
SLICC Concept
SLICC Ingredients
Results
Summary

## Slide 21: Experimental Evaluation
How does SLICC affect INSTRUCTION misses?
 Our primary goal
How does it affect DATA misses?
 Expected to increase, by how much?
Performance impact:
 Are DATA misses and MIGRATION OVERHEADS amortized?

## Slide 22: Methodology
Simulation
  Zesto (x86)
    16 OoO cores, 32KB L1-I, 32KB L1-D, 1MB per core L2
  QEMU extension
    User and Kernel space
Workloads
Shore-MT

## Slide 23: Effect on Misses
Baseline: no effort to reduce instruction misses
Better
Reduce I-MPKI by 58%. Increase D-MPKI by 7%.
I-MPKI
D-MPKI
Chart: MPKI
| Base | SLICC | SLICC-SW |  | Base | SLICC | SLICC-SW |  | Base | SLICC | SLICC-SW | TPC-C-10 |  | TPC-E |  | MapReduce
I-MPKI | 39.9829 | 25.843 | 17.5589 | 32.0774 | 17.1856 | 12.4782 | 5.81 | 5.8317 | 5.8317
D-MPKI | 32.6111 | 33.8937 | 32.9544 | 30.9176 | 33.2632 | 31.8984 | 1 | 0.9957 | 0.9957

## Slide 24: Performance
Next-line: always prefetch the next-line
Upper bound for Proactive Instruction Fetch [Ferdman, MICRO’11]
Chart: Speedup
| TPC-C-1 | TPC-C-10 | TPC-E | MapReduce
Next-Line | 1.192 | 1.185 | 1.173 | 0.99
PIF-No Overhead | 1.6392 | 1.5889 | 1.4705 | 1.03
SLICC | 1.4501 | 1.4626 | 1.5972 | 1.0056
SLICC-SW | 1.604 | 1.6135 | 1.79 | 1.0056
Better
TPC-C: +60% TPC-E: +79%
Storage per core
- PIF: ~40KB
- SLICC: <1KB.
Next-Line
PIF-No Overhead
SLICC
SLICC-SW

## Slide 25: Summary
OLTP’s performance suffers due to instruction stalls.
Technology & Application Opportunities:
Instruction footprint fits on aggregate L1-I capacity of CMPs.
Inter- and intra-thread locality.
SLICC:
Thread migration  spread instruction footprint over multiple cores.
Reduce I-MPKI by 58%
Improve performance by
Baseline: +70%
Next-line: +44%
PIF: ±2% to +21%

## Slide 26: Thanks!

## Slide 27: Why data misses increase?
Example: thread migrates from core A  core B.
    Read data on core B that is fetched on core A.
    Write data on core B to invalidate data on core A.
    When returning to core A, cache blocks might be evicted by other threads.

## Slide 28: SLICC Agent per Core

## Slide 29: Detailed Methodology
Zesto (x86)
Qtrace (QEMU extension)
Shore-MT

## Slide 30: Hardware Cost

## Slide 31: Larger I-caches?
Chart: MPKI
| 16 | 32 | 64 | 128 | 256 | 512 | 16 | 32 | 64 | 128 | 256 | 512 | 16 | 32 | 64 | 128 | 256 | 512 | 16 | 32 | 64 | 128 | 256 | 512 | 16 | 32 | 64 | 128 | 256 | 512 | 16 | 32 | 64 | 128 | 256 | 512 | Instructions |  | Data | Instructions |  | Data | Instructions |  | Data | TPC-C-10 |  | TPC-E |  | MapReduce
Compulsory | 0.22031 | 0.22031 | 0.22031 | 0.22031 | 0.22031 | 0.22031 | 28.7273 | 28.7273 | 28.7273 | 28.7273 | 28.7273 | 28.7273 | 0.067881 | 0.067881 | 0.067881 | 0.067881 | 0.067881 | 0.067881 | 28.8942 | 28.8942 | 28.8942 | 28.8942 | 28.8942 | 28.8942 | 2.0022 | 2.0022 | 2.0022 | 2.0022 | 2.0022 | 2.0022 | 6.4453 | 6.4453 | 6.4453 | 6.4453 | 6.4453 | 6.4453
Capacity | 47.6912 | 33.9369 | 12.1102 | 0.57967 | 0 | 0 | 2.594 | 1.3447 | 0.5399 | 0.34205 | 0.19621 | 0 | 51.2581 | 35.1609 | 2.4686 | 0 | 0 | 0 | 4.1403 | 1.0359 | 0.24528 | 0.18867 | 0.062271 | 0 | 3.5724 | 2.9071 | 1.61 | 0 | 0 | 0 | 0.74307 | 0.52538 | 0.31532 | 0 | 0 | 0
Conflict | 1.8744 | 0 | 1.2662 | 1.6101 | 0.19048 | 0.00094256 | 0.4368 | 0.096931 | 0 | 0 | 0 | 0 | 1.3701 | 0 | 2.4202 | 0.14519 | 0.0085356 | 0.00056146 | 0 | 0.70353 | 0.48139 | 0 | 0 | 0 | 0.077163 | 0 | 0 | 0.010581 | 0.052687 | 0.22138 | 0.38585 | 0.30011 | 0.35751 | 0.4574 | 0 | 0
Speedup | 0.93748 | 1 | 1.0844 | 1.1494 | 1.164 | 1.1658 | 0.98574 | 1 | 1.0069 | 1.0092 | 1.01 | 1.0131 | 0.94059 | 1 | 1.0913 | 1.1088 | 1.1098 | 1.1092 | 0.98562 | 1 | 1.0054 | 1.0096 | 1.0088 | 1.0104 | 0.97029 | 1 | 1.0193 | 1.0293 | 1.0293 | 1.0293 | 0.96817 | 1 | 1.0257 | 1.0258 | 1.0287 | 1.0297
Better
Better

## Slide 32: Different Replacement Policies?
Chart: L1 Instruction MPKI
| TPC-C | TPC-E | MapReduce
LRU | 33.4393 | 32.0803 | 5.81
LIP | 33.6886 | 31.3313 | 6.6901
BIP | 35.5644 | 32.9108 | 10.8239
DIP | 33.1629 | 30.4448 | 5.8174
SRRIP | 32.5829 | 30.3973 | 5.7015
BRRIP | 32.0672 | 28.8681 | 6.1645
DRRIP | 32.0199 | 28.8564 | 6.1887
Better

## Slide 33: Parameter Space (1)
Chart: Fill-up_t (top), Matched_t (bottom)
| Base | 128 | 256 | 384 | 512 | 128 | 256 | 384 | 512 | 128 | 256 | 384 | 512 | 128 | 256 | 384 | 512 | 128 | 256 | 384 | 512 | Base | 128 | 256 | 384 | 512 | 128 | 256 | 384 | 512 | 128 | 256 | 384 | 512 | 128 | 256 | 384 | 512 | 128 | 256 | 384 | 512 |  | 2 |  | 4 |  | 6 |  | 8 |  | 10 |  |  | 2 |  | 4 |  | 6 |  | 8 |  | 10 | TPC-C | TPC-E
I-MPKI | 33.4393 | 15.8164 | 15.2533 | 15.7238 | 15.108 | 15.952 | 15.1019 | 15.3836 | 15.6991 | 17.5422 | 17.7556 | 17.7924 | 17.926 | 19.9202 | 19.7568 | 20.0529 | 20.0529 | 21.7615 | 21.7615 | 21.9392 | 22.0672 | 32.0803 | 10.4767 | 10.5638 | 10.4114 | 10.2389 | 11.4389 | 11.5738 | 11.3499 | 11.9088 | 12.868 | 12.8439 | 12.3237 | 12.1657 | 13.7561 | 13.7177 | 13.8997 | 13.774 | 15.205 | 15.2515 | 15.2514 | 15.3299
D-MPKI | 30.1689 | 33.7956 | 33.8081 | 33.881 | 34.1311 | 36.9687 | 37.029 | 37.173 | 37.2073 | 38.1737 | 38.3581 | 38.3112 | 38.3331 | 38.81 | 38.9359 | 39.0192 | 39.0192 | 39.3272 | 39.3272 | 39.4695 | 39.4645 | 30.6336 | 33.5595 | 33.4854 | 33.6175 | 33.6637 | 36.69 | 36.6349 | 36.6892 | 36.6277 | 37.8275 | 37.866 | 37.8875 | 37.989 | 38.5871 | 38.4807 | 38.5386 | 38.5829 | 38.9311 | 38.9336 | 38.9776 | 38.9517
Speedup | 1 | 1.323 | 1.3381 | 1.3235 | 1.3356 | 1.3564 | 1.3567 | 1.3483 | 1.3473 | 1.2566 | 1.2424 | 1.2389 | 1.2412 | 1.156 | 1.1543 | 1.1456 | 1.1456 | 1.0797 | 1.0797 | 1.069 | 1.0696 | 1 | 1.4488 | 1.448 | 1.4522 | 1.4571 | 1.4679 | 1.4677 | 1.4685 | 1.4638 | 1.3812 | 1.3779 | 1.374 | 1.3638 | 1.2719 | 1.2802 | 1.2787 | 1.2699 | 1.2055 | 1.207 | 1.2003 | 1.2031
Better
Better

## Slide 34: Parameter Space (2)
Chart: Dilution_t
| 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20 | 22 | 24 | 26 | 28 | 30 | 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20 | 22 | 24 | 26 | 28 | 30 | TPC-C |  | TPC-E
I-MPKI | 15.1019 | 15.1019 | 14.871 | 14.1331 | 14.1112 | 13.7525 | 14.3469 | 14.0581 | 14.9413 | 14.9605 | 15.4751 | 16.1156 | 16.3853 | 16.4046 | 17.2782 | 17.9967 | 19.0571 | 19.0571 | 19.6761 | 20.3434 | 21.1946 | 21.6411 | 21.9602 | 23.0301 | 23.815 | 24.6413 | 25.5009 | 25.7189 | 26.5018 | 27.4577 | 11.5738 | 11.2555 | 10.4205 | 10.5099 | 10.3645 | 10.5621 | 11.001 | 11.1811 | 11.92 | 12.3554 | 12.7849 | 13.5216 | 14.0181 | 14.6028 | 15.2113 | 15.9827 | 16.5113 | 17.1908 | 17.9045 | 18.5014 | 19.3115 | 20.0538 | 20.866 | 21.5344 | 22.2327 | 23.1062 | 23.6379 | 24.3478 | 26.8406 | 34.398
D-MPKI | 37.029 | 37.029 | 36.364 | 35.8335 | 35.1328 | 34.6399 | 34.1749 | 33.8435 | 33.5069 | 33.4652 | 33.1559 | 32.8158 | 32.7709 | 32.7636 | 32.3574 | 32.3075 | 32.1773 | 32.1773 | 31.9976 | 31.6941 | 31.7446 | 31.5744 | 31.5357 | 31.4746 | 31.2255 | 31.1682 | 30.9792 | 30.8632 | 29.3432 | 27.4874 | 36.6349 | 36.3989 | 35.7983 | 34.9197 | 34.0496 | 33.4329 | 32.9437 | 32.5957 | 32.1519 | 31.7504 | 31.5343 | 31.172 | 31.1098 | 30.9644 | 30.8459 | 30.5986 | 30.6332 | 30.4392 | 30.2618 | 30.3718 | 30.1801 | 30.2983 | 29.9317 | 30.0383 | 29.5267 | 28.8868 | 28.2173 | 27.3235 | 24.1847 | 14.6689
Speedup | 1.3567 | 1.3567 | 1.3904 | 1.4252 | 1.4706 | 1.514 | 1.5497 | 1.575 | 1.5959 | 1.604 | 1.6222 | 1.6383 | 1.6416 | 1.635 | 1.6521 | 1.6476 | 1.6495 | 1.6495 | 1.652 | 1.664 | 1.6533 | 1.6534 | 1.6424 | 1.6399 | 1.6419 | 1.6406 | 1.6397 | 1.6453 | 1.551 | 1.4496 | 1.4677 | 1.4804 | 1.5273 | 1.5778 | 1.6427 | 1.6929 | 1.7267 | 1.7601 | 1.7801 | 1.803 | 1.8132 | 1.8304 | 1.8291 | 1.8326 | 1.8336 | 1.8423 | 1.8334 | 1.8426 | 1.8418 | 1.8353 | 1.8353 | 1.8234 | 1.835 | 1.8234 | 1.7625 | 1.6918 | 1.6061 | 1.5043 | 1.2305 | 0.79296
Better
Better

## Slide 35: Cache Signature Accuracy
Partial Bloom Filter
Chart: BF Accuracy
| 512 | 1K | 2K | 4K | 8K | 512 | 1K | 2K | 4K | 8K | TPC-C |  | TPC-E
Accuracy | 98.0098 | 98.7479 | 99.32 | 99.7295 | 99.8889 | 97.9254 | 98.744 | 99.2591 | 99.6516 | 99.8651
Better