## Slide 1
4 such LPDRAM
channels
N. Chatterjee, M. Shevgoor, R. Balasubramonian, A. Davis, Z. Fang*‡, R. Illikkal†, and R. Iyer†
University of Utah, Intel Labs† and Nvidia*(work done while at Intel) ‡
DRAM Variants
DDR3
DDR4
DDR2
DDR
LPDDR
RLDRAM
Heterogeneous Memory
Critical Word Regularity
Word-0 is the critical word 67% of the time
Fetch Critical-Word from RLDRAM
Fetch Non-Critical words from LPDDR
Average gap between first and second access > LPDDR latency 82% of the time
Processor
64-bit Data + ECC
MC0
23-bit Addr/Cmd
RLMC
LPDRAM DIMM 1.75GB Data+ ECC
4 Sub-Ranked Channels of RLDRAM, each 0.25GB Data
38-bit Addr/Cmd
8-bit Data + 1-bit parity RLDRAM Channel
Ch0
Ch1
Ch2
Ch3
4 such LPDDR channels
RLDRAM/LPDDR Heterogeneous Memory
Processor
MC0
64-bit Data +ECC
23-bit Addr/Cmd
MRC0
8-bit Data + 1-bit Parity
26-bit Addr/Cmd
LPDRAM DIMM 1.75GB Data+ ECC (4 such channels)
RLDRAM 0.25GB Data
4 such Data and Add/Cmd Channels
Results
Average performance improvement of 12.9%
22% reduction in average Latency
Memory energy reduction of 15%
System energy reduction of 6%
Leveraging Heterogeneity in DRAM Main Memories to Accelerate Critical Word Access
Processor
MC0
2GB DDR3 DRAM DIMM
72-bit Data
+ECC
23-bit Addr/Cmd
4 such DDR3
channels
(a) Baseline DDR3 System
(b) Heterogeneous System with Critical Word Access
(c) Proposed System
Heterogeneous memory system includes low-latency RLDRAM and low-energy LPDRAM
Average main memory access time of RLDRAM3 is 43% lower than that of DDR3
Chart: mW
| DDR3 | RLDRAM3 | LPDDR2
Activate | 230 | 400 | 65
RD-WR/Terminate | 125 | 125 | 89
Background | 55 | 250 | 43