## Slide 1: NoRD: Node-Router Decoupling for Effective Power-gating of On-Chip Routers
Lizhong Chen and Timothy M. Pinkston
SMART Interconnects Group
University of Southern California
December 4, 2012

## Slide 2: NoC Power Consumption
  Chip power has become a main design constraint
  High power consumption in the NoC
  Static power increasing in on-chip routers
  Various contributors to router static power
Canonical router at 45nm and 1.0V
Notes: Power: Chip -> NoC

## Slide 3: Use of Power-gating
Applications of power-gating
  Save static power by cutting off power supply to block
  Have been applied to cores and execution units
  Few works on applying it to on-chip routers
Objectives of power-gating
  Maximize net energy savings
  Minimize performance penalty
Proposed Node-Router Decoupling
  Increase power-gating opportunity
  and effectiveness in on-chip networks

## Slide 4: Conventional Use of Power-gating Applied to NoC Routers
Power off the router
  When the datapath of the router is empty, and
  After notifying all of its neighbors (PG signal)
Awake the router when
  Any neighbors assert WU signal
  Neighbors wait for PG signal to clear
Effectiveness subject to
  Wakeup latency (~12 cycles for router)
  Breakeven-time (BET)
    The minimum number of consecutive gated-off idle cycles to offset power-gating energy overhead (~10 cycles for router)
WU
PG
Router
A
Router
B
Router
D
WU
PG
Router
C
WU
PG
Router
E
WU
PG

## Slide 5: Challenges in Conventional Use of Power-gating to NoC Routers
BET limitation is intensified
  Intermittent packet arrivals => fragmented idle intervals
Cumulative wakeup latency in multi-hop NoCs
  Worse for larger networks
Disconnection problem
  Idle period is upper bounded by
  local node’s traffic
  Disconnected network
2
0
1
3
4
5
6
7
8
9
10
11
12
13
14
15
S
D
Full system simulation on PARSEC shows that 61% of the total number of idle periods has length less than BET!
Conventional use of power gating to NoC routers can have limited effectiveness

## Slide 6: Node-Router Decoupling in a Nutshell
Node 2
  Break node-router dependence through decoupling bypass paths
  Add two bypass paths to each router
  On the chip-level: form a bypass ring connecting all nodes
  Bypass Inport => NI ejection, NI injection => Bypass Outport
NI = Network Interface
2
0
1
3
4
5
6
7
8
9
10
11
12
13
14
15
S
D
1
3
4
Mitigate BET limitation
  Use bypass paths instead of waking up routers
Hide wakeup latency
  Use bypass paths while routers are waking up
Eliminate disconnection
  All nodes are always connected by the bypass ring

## Slide 7: Outline
Introduction, motivation, basic idea
Node-router decoupling implementation
Evaluation methodology and results
Related work
Summary

## Slide 8: On-chip Networks
NoC-based architecture
Canonical Router architecture
Network Interface (NI)
Core, Cache,
Memory Controller
Notes: Role of NI

## Slide 9: NoRD Bypass Paths
Add two bypass paths to each router
  One bypass from Bypass Inport to the NI ejection
  One bypass from the NI injection to Bypass Outport
State-transitions
  On -> off, when the datapath of router is empty
  Off -> on, when a wakeup metric exceeds a threshold
    VC request rate at the local NI
①
③
Network Interface
Low implementation cost of decoupling bypass paths and forwarding logic: 3.1% of router area

## Slide 10: NoRD Routing
Based on Duato’s Protocol for fully adaptive routing
  Minimal path along gated-on routers & gated-off routers
2
0
1
3
4
5
6
7
8
9
10
11
12
13
14
15
S
D
D

## Slide 11: NoRD Routing
Based on Duato’s Protocol for Fully Adaptive Routing
  Minimal path along gated-on routers & gated-off routers
  Limited misroutes possible only if all routers off along min path
  Bypass Ring serves as “escape path”
2
0
1
3
4
5
6
7
8
9
10
11
12
13
14
15
S
D
D
Notes: Explain DP, max hop, if 8 is on; if not, then

## Slide 12: Increasing NoRD Efficiency
2
0
1
3
4
5
6
7
8
9
10
11
12
13
14
15
2
0
1
3
4
5
6
7
8
9
10
11
12
13
14
15
Differentiate routers
  Routers have different impact on performance based on their locations in the NoC
2
0
1
3
4
5
6
7
8
9
10
11
12
13
14
15

## Slide 13: Increasing NoRD Efficiency
Differentiate routers
  Routers have different impact on performance based on their locations in the NoC
Performance-centric class vs. Power-centric class
  Wake up early a few performance-critical
  routers to add “shortcuts” in routing
  Wake up late the rest (majority) of the
  routers to save more static power
  Use an off-line program to classify
  the routers
2
0
1
3
4
5
6
7
8
9
10
11
12
13
14
15
Notes: Wake up early a few performance-critical routers to improve performance by adding “shortcuts” in routing
Wake up late the rest (majority) of the routers to save more static power by allowing those routers to stay in gated-off state for a longer time
NoRD enables this trade-off

## Slide 14: Evaluation Methodology
Simulation platform
  Platform: Simics + Gems (Garnet+Orion2.0)
  Workloads: PARSEC 2.0 + Synthetic traffic
Key parameters for simulations | 
Core model | Sun UltraSPARC III+, 3GHz
Private I/D L1$ | 32KB, 2-way, LRU, 1-cycle latency
Shared L2 per bank | 256KB, 16-way, LRU, 6-cycle latency
Cache block size | 64Bytes
Coherence protocol | MOESI
Network topology | 4x4 and 8x8 mesh
Router | 4-stage, 3GHz
Virtual channel | 4 per protocol class
Input buffer | 5-flit depth
Link bandwidth | 128 bits/cycle
Memory controllers | 4, located one at each corner
Memory latency | 128 cycles

## Slide 15: Schemes Under Comparison
No power-gating (No_PG)
Conventional power-gating (Conv_PG)
  Apply power-gating technique conventionally to routers
Optimized conventional power-gating (Conv_PG_OPT)
  Conv_PG + early wakeup (hide some wakeup latency)
Node-router decoupling (NoRD)
  Power-gate routers and enable bypass paths when load is low
  When load becomes high, routers are powered on gradually

## Slide 16: Static Energy Comparison
Static energy saved
  Conv_PG: 51.2%, Conv_PG_OPT : 47.0%
  NoRD: 62.9%
  Relative improvement of NoRD: 23.9% and 29.9%

## Slide 17: Power-gating Overhead Reduction
NoRD reduces power-gating overhead and number of router wakeups by over 80%
  Power-gating Overhead Reduction in # of router wakeups

## Slide 18: Overall NoC Energy
Overall NoC energy saved
  Conv_PG: 9.4%, Conv_PG_OPT: 9.1%, NoRD: 20.6%
  Static energy savings exceed dynamic energy losses
Notes: Discuss misrouting

## Slide 19: Performance
Average packet latency penalty
  Conv_PG: 63.8%, Conv_PG_OPT: 41.5%, NoRD: 15.2%
Execution time penalty
  Conv_PG: 11.7%, Conv_PG_OPT: 8.1%, NoRD: 3.9%
  Average packet latency Execution time
Notes: Misrouting and PG

## Slide 20: Related Work
Applications of power-gating in CMPs
  Apply to cores and execution units in CMPs (Z. Hu, et al., 2004; A. Lungu, et al., 2009; N. Madan, et al., 2011; others)
  Apply power-gating conventionally to on-chip routers (H. Matsutani, et al., 2008; S.Jafri, et al., 2010, H. Matsutani, et al., 2010)
  Effectiveness is limited by the BET requirement, wakeup delay and disconnection problem
Other uses of bypass
  For fault-tolerance: work for infrequent on/off transitions (M. Koibuchi, et al., 2008; J. Kim, et al., 2006; others)
  For express channels: improve performance and dynamic power (W. Dally, 1991; A. Kumar, et al., 2007; B. Grot, et al., 2009; others)
  For reducing power consumption in links (E. Kim, et al., 2003; V. Soteriou, et al., 2004; B. Zafar, et al., 2010; others)
  These techniques are either not suitable for run-time router power-gating or have different targets, thus being orthogonal to this work

## Slide 21: Summary
Node-router dependence severely limits the use of power-gating in on-chip routers
  BET limitation, wakeup delay and disconnection problem
A novel approach, Node-Router Decoupling (NoRD), is proposed based on power-gating bypass paths
  Significantly reduces the number of power state transitions
  Increases the length of idle periods
  Completely hides the wakeup latency from the critical path
  Eliminates network disconnection problems
NoRD increases power-gating opportunity while minimizing performance overhead

## Slide 22
Thank you!

## Slide 23: Power-gating Basics
Breakeven-time (BET)
  The minimum number of consecutive gated-off idle cycles to offset power-gating energy overhead
  Around 10 cycles for router
Wakeup latency
  Around 10~15 cycles for router
time

## Slide 24: NoRD Routing
Based on Duato’s Protocol
  Escape resources are comprised of escape VCs of the bypass ring formed by (Bypass Inport, Bypass Outport) pairs
  Other VCs are adaptive resources
Packets on adaptive VCs
  First routed minimally
  If not possible, detoured by one
    May still routed on adaptive VCs
  If misrouted hops reach threshold
    Forced to enter escape VCs
Packets on escape VCs
  Confined to bypass ring until destination
2
0
1
3
4
5
6
7
8
9
10
11
12
13
14
15
S
D
D
Notes: Explain DP, max hop, if 8 is on; if not, then