## Slide 1: MorphCore: An Energy-Efficient Architecture for High-Performance ILP and High-Throughput TLP
Khubaib*
M. Aater Suleman*+ Milad Hashemi*
Chris Wilkerson‡ Yale N. Patt*
* HPS Research Group
The University of Texas at Austin
+ Calxeda Inc.
‡ Intel Labs

## Slide 2: The Need for an Adaptive Core
Sometimes a single thread with high ILP
  Need a heavy-weight out-of-order core
  Provides high performance by exploiting ILP
Sometimes many threads
  Out-of-order is unnecessary
  Need a power-efficient core
  Provides high performance by exploiting thread-level parallelism
We need an adaptive core that can do both
  Exploits instruction-level parallelism when needed
  Exploits thread-level parallelism when needed

## Slide 3: Problem
Large cores
  Good: High single-thread performance
  Bad: Inefficient when TLP is available
Small cores
  Good: High multithreaded performance
  Bad: Poor single thread performance
Current core architectures do not adapt
Large cores limit performance when TLP is high
Small cores limit performance when TLP is low

## Slide 4: Outline
Problem Statement
Previous Work
  Asymmetric chip multiprocessors
  Reconfigurable core architectures
MorphCore
Evaluation

## Slide 5: Asymmetric Chip Multiprocessors
One or few large out-of-order cores with many small in-order cores [Morad+ CAL’06, Suleman+ TR’07, Hill+ Computer’07, Suleman+ ASPLOS’09]
  Limited flexibility
    Fixed number of large and small cores
  Migration overhead
    Migrate the thread state/data to large core

## Slide 6: Reconfigurable Core Architectures
Fundamental Idea
  Build a chip with “simpler cores” and “combine” them at runtime using additional logic to form a high-performance out-of-order core
  Core Fusion - Ipek+ ISCA’07, TFlex - Kim+ MICRO’07, Federation Cores - Tarjan+ DAC’08, and many others
Fused core has low performance and low energy-efficiency
  Increased latencies among its pipeline stages
Significant mode switching overhead

## Slide 7: Outline
Problem Statement
Previous Work
MorphCore
  Key Insights and Basic Idea
  Design and Operation
Evaluation

## Slide 8: Key Insight 1: The Potential of In-Order SMT
Chart: Number of SMT threads on the core
out-of-order | 1 | 1.6805 | 1.85 | 1.9169 | 1.9371 | 1.9572 | 1.958 | 1.9587
in-order | 0.4614 | 0.8919 | 1.3 | 1.5355 | 1.7 | 1.8385 | 1.878 | 1.9175
With 8 threads, the in-order core’s performance almost matches the out-of-order core’s
Black-Scholes
Program

## Slide 9: Key Insight 2
Minimal changes to a traditional OOO core can transform it into a highly-threaded in-order SMT core
Existing structures in an OOO core can be re-used to support highly-threaded in-order SMT execution

## Slide 10: MorphCore: Basic Idea
A) The base design: OOO core
out-of-order core
Exploits ILP
High single-thread performance
InOrder
highly-threaded in-order SMT core
Exploits TLP
High multi-thread performance
No OOO execution  Energy savings
OutOfOrder
Two modes:
The opposite of previous proposals:
B) Then we add in-order SMT

## Slide 11: Outline
Problem Statement
Previous Work
MorphCore
  Key Insights and Basic Idea
  Design and Operation
Evaluation

## Slide 12: Baseline OOO Pipeline
FETCH +
DECODE
RENAME +
Insert in RS
SELECT +
WAKEUP
REG
READ
EXE
COMMIT
Branch
Pred
+
I-cache
2-way SMT
Alloc
ROB
STQ
RS Free List
RS
OOO
Select + Wakeup
Physical Reg File
(PRF)
Store Buffer
D-cache
ALUs
LDQ/
STQ Lookup
ROB Commit
Speculative
RATs
Permanent
RATs
LDQ

## Slide 13: MorphCore Pipeline

## Slide 14: MorphCore Pipeline
Permanent
RATs
FETCH +
DECODE
RENAME +
Insert in RS
SELECT +
WAKEUP
REG
READ
EXE
COMMIT
Branch
Pred
+
I-cache
2-way SMT
RS Free List
RS
OOO
Select + Wakeup
Physical Reg File
(PRF)
LDQ/
STQ Lookup
ROB Commit
Speculative
RATs
8-way SMT
Alloc
ROB
STQ
LDQ
LDQ Alloc
RS FIFO Insert
In-Order Select + Wakeup
STQ Lookup
Store Buffer
D-cache
ALUs
LDQ Lookup
Delayed write back into PRF
Shared
OOO Only
In-order Only
Concatenate TID with Arch RegID

## Slide 15: Microarchitecture Summary
Use existing structures without modification
  Physical Register File (PRF), Decode, Execution pipeline
Use existing structures with minor modification
  OOO Reservation Stations  InOrder instruction queues
  Because of InOrder execution, delayed writeback into PRF (extra bypass)
SMT related changes
  Front-end (e.g. multiple PCs, branch history regs), changes in resource allocation algorithms
In-Order instruction scheduler

## Slide 16: Overheads
Core area increases by 1.5%
  Increase in SMT contexts (0.5%) (Note that added contexts are in-order, so no additional rename tables and physical registers)
  InOrder Wakeup and Select Logic (0.5%)
  Extra bypass (0.5%)
Core frequency decreases by 2.5%
  Add multiplexers in the critical path of 2 stages
    Rename and Scheduling

## Slide 17: Mode Switching Policy
Number of active threads ≤ 2 ?
OutofOrder when active threads ≤ 2
  MorphCore can support up to 2 OOO threads
  TLP is limited so execute OOO to obtain performance
InOrder when active threads > 2
  More than 2 threads can only run simultaneously in InOrder mode
  TLP is high so high core throughput and energy savings can be obtained by executing threads in-order

## Slide 18: How Mode Switching Happens?
  (1) Drains the core pipeline
  (2) Spills architectural registers of currently active threads to reserved ways in the private 256KB L2
  (3) Turns off/on Renaming, OOO Scheduling, Load Queue
  (4) Fills the architectural registers of next-active threads into PRF (update RATs when going into OutofOrder)
Currently an overhead of 300 - 450 cycles

## Slide 19: Outline
Problem Statement
Previous Work
MorphCore
Evaluation

## Slide 20: Methodology
Detailed cycle-level x86 simulator
McPAT (modified) to calculate energy/area
Performance/energy evaluation of MorphCore vs. alternative architectures
  Large OOO cores: optimized for single-thread
  Medium and Small cores: optimized for multi-thread
Workloads
  Single-threaded (ST): 14 – SPEC 2006
  Multi-threaded (MT): 14 – Databases, SPLASH, others
Notes: We use a detail cycle-level x86 simulator. We modified mcpat to calculate energy and area. We compare MorphCore’s performance and energy consumption against 4 alternative architectures. 2 large OOO core architectures which are optimized for single-thread performance, and 2 medium and small core architectures which are optimized for MT. we evaluate using 14 single-thread workloads from SPEC 2006, and 14 MT workloads from various domains including databases and SPLASH.

## Slide 21: Evaluated Architectures
Core | # of cores | Freq. (GHz) | Type | Issue width | SMT threads Per core | Total threads | Peak throughput ops/cycle ST MT
OOO-2 | 1 | 3.4 | OOO | 4 | 2 | 2 | 4 4
OOO-4 | 1 | -5% | OOO | 4 | 4 | 4 | 4 4
MED | 3 | same | OOO | 2 | 1 | 3 | 2 6
SMALL | 3 | same | InO | 2 | 2 | 6 | 2 6
MorphCore | 1 | -2.5% | OOO/ InO | 4 | 2 OOO/ 8 InO | 2 OOO/ 8 InO | 4 4
  All comparisons on approximately equal area
  ST : single-thread MT: multi-thread
  OOO : out-of-order InO : in-order

## Slide 22: Evaluated Architectures
Core | # of cores | Freq. (GHz) | Type | Issue width | SMT threads Per core | Total threads | Peak throughput ops/cycle ST MT
OOO-2 | 1 | 3.4 | OOO | 4 | 2 | 2 | 4 4
OOO-4 | 1 | -5% | OOO | 4 | 4 | 4 | 4 4
MED | 3 | same | OOO | 2 | 1 | 3 | 2 6
SMALL | 3 | same | InO | 2 | 2 | 6 | 2 6
MorphCore | 1 | -2.5% | OOO/ InO | 4 | 2 OOO/ 8 InO | 2 OOO/ 8 InO | 4 4
  All comparisons on approximately equal area
  ST : single-thread MT: multi-thread
  OOO : out-of-order InO : in-order

## Slide 23: Evaluated Architectures
Core | # of cores | Freq. (GHz) | Type | Issue width | SMT threads Per core | Total threads | Peak throughput ops/cycle ST MT
OOO-2 | 1 | 3.4 | OOO | 4 | 2 | 2 | 4 4
OOO-4 | 1 | -5% | OOO | 4 | 4 | 4 | 4 4
MED | 3 | 3.4 | OOO | 2 | 1 | 3 | 2 6
SMALL | 3 | 3.4 | InO | 2 | 2 | 6 | 2 6
MorphCore | 1 | -2.5% | OOO/ InO | 4 | 2 OOO/ 8 InO | 2 OOO/ 8 InO | 4 4
  All comparisons on approximately equal area
  ST : single-thread MT: multi-thread
  OOO : out-of-order InO : in-order

## Slide 24: Evaluated Architectures
Core | # of cores | Freq. (GHz) | Type | Issue width | SMT threads Per core | Total threads | Peak throughput ops/cycle ST MT
OOO-2 | 1 | 3.4 | OOO | 4 | 2 | 2 | 4 4
OOO-4 | 1 | -5% | OOO | 4 | 4 | 4 | 4 4
MED | 3 | 3.4 | OOO | 2 | 1 | 3 | 2 6
SMALL | 3 | 3.4 | InO | 2 | 2 | 6 | 2 6
MorphCore | 1 | -2.5% | OOO/ InO | 4 | 2 OOO/ 8 InO | 2 OOO/ 8 InO | 4 4
  All comparisons on approximately equal area
  ST : single-thread MT: multi-thread
  OOO : out-of-order InO : in-order

## Slide 25: Evaluated Architectures
Core | # of cores | Freq. (GHz) | Type | Issue width | SMT threads Per core | Total threads | Peak throughput (ops/cycle) ST MT
OOO-2 | 1 | 3.4 | OOO | 4 | 2 | 2 | 4 4
OOO-4 | 1 | -5% | OOO | 4 | 4 | 4 | 4 4
MED | 3 | 3.4 | OOO | 2 | 1 | 3 | 2 6
SMALL | 3 | 3.4 | InO | 2 | 2 | 6 | 2 6
MorphCore | 1 | -2.5% | OOO/ InO | 4 | 2 OOO/ 8 InO | 2 OOO/ 8 InO | 4 4
  All comparisons on approximately equal area
  ST : single-thread MT: multi-thread
  OOO : out-of-order InO : in-order

## Slide 26: Performance: Single-thread
Chart: 
| ST_Avg | MT_Avg | All_Avg
OOO-2 | 1 | 1 | 1
OOO-4 | 0.9752 | 1.1516 | 1.0598
MorphCore | 0.9878 | 1.2265 | 1.1007
MED | 0.7437 | 1.3083 | 0.9864
SMALL | 0.4035 | 1.3383 | 0.7349
MorphCore: -1.2%
MED: -25%
SMALL: -59%

## Slide 27: Performance: Multi-thread
Chart: 
| ST_Avg | MT_Avg | All_Avg
OOO-2 | 1 | 1 | 1
OOO-4 | 0.9752 | 1.1516 | 1.0598
MorphCore | 0.9878 | 1.2265 | 1.1007
MED | 0.7437 | 1.3083 | 0.9864
SMALL | 0.4035 | 1.3383 | 0.7349
MorphCore: +22%
MED: +30%
SMALL: +33%

## Slide 28: Performance: Both ST and MT
Chart: 
| ST_Avg | MT_Avg | All_Avg
OOO-2 | 1 | 1 | 1
OOO-4 | 0.9752 | 1.1516 | 1.0598
MorphCore | 0.9878 | 1.2265 | 1.1007
MED | 0.7437 | 1.3083 | 0.9864
SMALL | 0.4035 | 1.3383 | 0.7349
MorphCore over OOO-2: +10%
over OOO-4: +4%
over MED: +11%
over SMALL: +49%

## Slide 29: Energy
Chart: 
| ST_Avg | MT_Avg | ALL_Avg
OOO-2 | 1 | 1 | 1
OOO-4 | 1.0622 | 0.9888 | 1.0419
MorphCore | 1.0251 | 0.9125 | 0.9939
MED | 0.6989 | 0.9744 | 0.7822
SMALL | 0.5461 | 0.815 | 0.6206
For MT workloads, MorphCore is the second-best in energy-efficiency
Consumes 9% less energy than OOO-2

## Slide 30: Energy-delay-squared (ED2)
Chart: 
| ST_Avg | MT_Avg | ALL_Avg
OOO-2 | 1 | 1 | 1
OOO-4 | 1.1168 | 0.7268 | 0.901
MorphCore | 1.0509 | 0.5786 | 0.7798
MED | 1.2918 | 0.5631 | 0.8639
SMALL | 3.5228 | 0.4211 | 1.218
3.5
On average, across all workloads, MorphCore provides the lowest ED2
22% lower than OOO-2 and 44% lower than SMALL

## Slide 31: Summary
MorphCore adapts well to both single-thread and multi-thread workloads
Requires minimal changes to a traditional OOO core
Operates in two modes:
  OOO core when TLP is low
  Highly-threaded in-order SMT core when TLP is high
Significantly outperforms other alternative architectures

## Slide 32: MorphCore: An Energy-Efficient Architecture for High-Performance ILP and High-Throughput TLP
Khubaib*
M. Aater Suleman*+ Milad Hashemi*
Chris Wilkerson‡ Yale N. Patt*
* HPS Research Group
The University of Texas at Austin
+ Calxeda Inc.
‡ Intel Labs