## Slide 1: Composite Cores: Pushing Heterogeneity into a Core
Andrew Lukefahr, Shruti Padmanabha, Reetuparna Das, Faissal M. Sleiman, Ronald Dreslinski, Thomas F. Wenisch, and Scott Mahlke
University of Michigan
Micro 45
May 8th 2012

## Slide 2: High Performance Cores
High performance cores waste energy on low performance phases
Different phases can have very different performance on the same hardware
Performance
Energy
Time
High energy yields high performance
Low performance DOES NOT yield low energy

## Slide 3: Core Energy Comparison
Brooks, ISCA’00
Dally, IEEE Computer’08
Out-of-Order
In-Order
Out-Of-Order contains performance enhancing hardware
  Not necessary for correctness
Do we always need the extra hardware?

## Slide 4: Previous Solution: Heterogeneous Multicore
2+ Cores
Same ISA, different implementations
  High performance, but more energy
  Energy efficient, but less performance
Share memory at high level
  Share L2 cache ( Kumar ‘04)
  Coherent L2 caches (ARM’s big.LITTLE)
Operating System (or programmer) maps application to smallest core that provides needed performance

## Slide 5: Current System Limitations
Migration between cores incurs high overheads
  20K cycles (ARM’s big.LITTLE)
Sample-based schedulers
  Sample different cores performances and then decide whether to reassign the application
  Assume stable performance with a phase
Phase must be long to be recognized and exploited
  100M-500M instructions in length
Do finer grained phases exist?
Can we exploit them?

## Slide 6: Performance Change in GCC
Average IPC over a 1M instruction window (Quantum)
Average IPC over 2K Quanta
Huge performance changes within a quantum!
Chart: Instructions
Chart: Instructions
Notes: Define quantum

## Slide 7: Finer Quantum
20K instruction window from GCC
Average IPC over 100 instruction quanta
What if we could map these to a Little Core?
Chart: Instructions

## Slide 8: Our Approach: Composite Cores
Hypothesis: Exploiting fine-grained phases allows more opportunities to run on a Little core
Problems
  How to minimize switching overheads?
  When to switch cores?
Questions
  How fine-grained should we go?
  How much energy can we save?

## Slide 9: Problem I: State Transfer
Fetch
Decode
Rename
O3
Execute
dTLB
dCache
Reg File
iCache
Branch Pred
iTLB
Decode
InO
Execute
Fetch
iCache
Branch Pred
iTLB
dTLB
dCache
RAT
Reg File
10s of KB
<1 KB
10s of KB
State transfer costs can be very high:
  ~20K cycles (ARM’s big.LITTLE)
Limits switching to coarse granularity:
100M Instructions ( Kumar’04)

## Slide 10: Creating a Composite Core
dTLB
dCache
RAT
Reg File
Decode
O3 Execute
dCache
dTLB
Fetch
iCache
Branch Pred
iTLB
Decode
inO Execute
Reg File
Mem
Load/Store Queue
Fetch
iCache
Branch Pred
iTLB
iCache
Branch Pred
iTLB
Fetch
Controller
dTLB
dCache
<1KB
Big
uEngine
Little
uEngine
Only one uEngine active at a time
Notes: Define uEngine somewhere

## Slide 11: Hardware Sharing Overheads
Big uEngine needs
  High fetch width
  Complex branch prediction
  Multiple outstanding data cache misses
Little uEngine wants
  Low fetch width
  Simple branch prediction
  Single outstanding data cache miss
Must build shared units for Big uEngine
  over-provision for Little uEngine
Assume clock gating for inactive uEngine
  Still has static leakage energy
Little pays ~8% energy overhead to use over provisioned fetch + caches

## Slide 12: Problem II: When to Switch
  Goal: Maximize time on the Little uEngine subject to maximum performance loss
    User-Configurable
Traditional OS-based schedulers won’t work
  Decisions to frequent
  Needs to be made in hardware
Traditional sampling-based approaches won’t work
  Performance not stable for long enough
  Frequent switching just to sample wastes cycles

## Slide 13: What uEngine to Pick
This value is hard to determine a priori, depends on application
  Use a controller to learn appropriate value over time
Run on Big
Run on Little
Chart: Instructions
Run on Big
Run on Little
Let user configure the target value

## Slide 14: Reactive Online Controller
Little uEngine
True
Big uEngine
False
Switching Controller
Big Model
+
Threshold
Controller
Little Model
User-Selected Performance

## Slide 15: uEngine Modeling
while(flag){
foo();
flag = bar();
}
Little uEngine
IPC: 1.66
IPC: ???
Big uEngine
Collect Metrics of active uEngine
iL1, dL1 cache misses
L2 cache misses
Branch Mispredicts
ILP, MLP, CPI
Use a linear model to estimate inactive uEngine’s performance
IPC: 2.15

## Slide 16: Evaluation
Architectural Feature | Parameters
Big uEngine | 3 wide O3 @ 1.0GHz 12 stage pipeline 128 ROB Entries 128 entry register file
Little uEngine | 2 wide InOrder @ 1.0GHz 8 stage pipeline 32 entry register file
Memory System | 32 KB L1 i/d cache, 1 cycle access 1MB L2 cache, 15 cycle access 1GB Main Mem, 80 cycle access
Controller | 5% performance loss relative to all big core

## Slide 17: Little Engine Utilization
Chart: Quantum Length (Instructions)
| 100 | 200 | 300 | 500 | 800 | 1000 | 2000 | 5000 | 8000 | 10000 | 50000 | 100000 | 500000 | 1000000 | 5000000 | 10000000
astar | 0.78003 | 0.72289 | 0.6884 | 0.64478 | 0.60611 | 0.58858 | 0.5379 | 0.48216 | 0.45932 | 0.44996 | 0.41565 | 0.4088 | 0.3955 | 0.389 | 0.37 | 0.36
bzip2 | 0.24271 | 0.22781 | 0.22205 | 0.21139 | 0.20039 | 0.1971 | 0.19008 | 0.18444 | 0.1823 | 0.18155 | 0.1782 | 0.1773 | 0.1755 | 0.175 | 0.17 | 0.17
gcc | 0.50357 | 0.44226 | 0.41298 | 0.38404 | 0.36313 | 0.35503 | 0.3364 | 0.31896 | 0.31148 | 0.30842 | 0.28495 | 0.2781 | 0.268 | 0.264 | 0.25 | 0.25
gobmk | 0.60891 | 0.53744 | 0.49819 | 0.45441 | 0.42106 | 0.4073 | 0.37317 | 0.34234 | 0.3304 | 0.32594 | 0.3033 | 0.2965 | 0.284 | 0.28 | 0.275 | 0.27
h264ref | 0.17138 | 0.15581 | 0.14798 | 0.13906 | 0.13498 | 0.13381 | 0.12893 | 0.12194 | 0.11878 | 0.11734 | 0.11045 | 0.1069 | 0.1015 | 0.1 | 0.095 | 0.09
hmmer | 0.27598 | 0.21391 | 0.19197 | 0.17394 | 0.16077 | 0.15549 | 0.14374 | 0.13715 | 0.13452 | 0.13348 | 0.12875 | 0.1261 | 0.1165 | 0.112 | 0.1 | 0.1
mcf | 0.98405 | 0.98111 | 0.97972 | 0.97823 | 0.97708 | 0.97659 | 0.97527 | 0.97361 | 0.97271 | 0.97236 | 0.96985 | 0.9689 | 0.9665 | 0.945 | 0.84 | 0.81
omnetpp | 0.3924 | 0.33084 | 0.30052 | 0.26543 | 0.23568 | 0.22263 | 0.1955 | 0.17906 | 0.17292 | 0.17041 | 0.15695 | 0.1522 | 0.144 | 0.142 | 0.14 | 0.13
sjeng | 0.55382 | 0.47204 | 0.43206 | 0.38757 | 0.35437 | 0.34181 | 0.30952 | 0.27857 | 0.26615 | 0.26107 | 0.24365 | 0.2388 | 0.2295 | 0.227 | 0.22 | 0.22
average | 0.50143 | 0.45379 | 0.43043 | 0.40432 | 0.38373 | 0.37537 | 0.3545 | 0.33536 | 0.32762 | 0.3245 | 0.31019 | 0.30596 | 0.29789 | 0.29267 | 0.27333 | 0.26667
3-Wide O3 (Big) vs. 2-Wide InOrder (Little)
5% performance loss relative to all Big
More time on little engine with same
performance loss
Traditional OS-Based Quantum
Fine-Grained Quantum

## Slide 18: Engine Switches
Chart: Quantum Length (Instructions)
| 100 | 200 | 300 | 500 | 800 | 1000 | 2000 | 5000 | 8000 | 10000 | 50000 | 100000 | 500000 | 1000000 | 5000000 | 10000000
astar | 2774.891 | 1711.365 | 1274.295 | 865.307 | 599.031 | 501.357 | 283.935 | 129.259 | 84.829 | 68.925 | 14.177 | 7.083 | 1.419 | 0.705 | 0.141 | 0.069
bzip2 | 3275.381 | 1617.675 | 1047.381 | 611.533 | 372.411 | 295.345 | 144.203 | 56.619 | 35.121 | 28.119 | 5.757 | 2.849 | 0.553 | 0.271 | 0.055 | 0.027
gcc | 4095.274 | 2122.295 | 1420.437 | 849.494 | 524.944 | 416.654 | 204.344 | 80.372 | 50.236 | 40.468 | 7.94 | 3.92 | 0.786 | 0.38 | 0.074 | 0.038
gobmk | 4042.18 | 2286.075 | 1608.059 | 1012.443 | 650.464 | 523.352 | 262.656 | 105.265 | 65.025 | 51.748 | 10.061 | 4.997 | 0.979 | 0.488 | 0.096 | 0.047
h264ref | 2334.499 | 1126.085 | 704.285 | 397.705 | 240.659 | 194.699 | 97.003 | 37.583 | 23.155 | 18.613 | 3.799 | 1.845 | 0.363 | 0.181 | 0.037 | 0.019
hmmer | 4147.845 | 1767.231 | 1085.501 | 604.911 | 353.443 | 271.815 | 121.573 | 45.983 | 28.191 | 22.415 | 4.569 | 2.317 | 0.445 | 0.217 | 0.041 | 0.021
mcf | 124.689 | 62.609 | 41.199 | 24.099 | 14.821 | 11.675 | 5.781 | 2.419 | 1.621 | 1.343 | 0.549 | 0.455 | 0.145 | 0.107 | 0.061 | 0.033
omnetpp | 4114.222 | 2052.843 | 1384.485 | 840.979 | 505.377 | 381.359 | 169.197 | 64.163 | 39.371 | 31.179 | 6.037 | 2.979 | 0.583 | 0.289 | 0.057 | 0.029
sjeng | 4523.579 | 2445.293 | 1706.947 | 1046.183 | 653.973 | 521.787 | 261.029 | 101.451 | 61.211 | 48.229 | 9.369 | 4.645 | 0.915 | 0.457 | 0.089 | 0.045
average | 3270.2844 | 1687.9412 | 1141.3988 | 694.7393 | 435.0137 | 346.4492 | 172.1912 | 69.2349 | 43.1956 | 34.5599 | 6.9176 | 3.4544 | 0.68756 | 0.34389 | 0.072333 | 0.036444
Need LOTS of switching to maximize utilization
~1 Switch / 2800 Instructions
~1 Switch / 306 Instructions

## Slide 19: Performance Loss
Chart: Quantum Length (Instructions)
| 100 | 200 | 300 | 500 | 800 | 1000 | 2000 | 5000 | 8000 | 10000 | 50000 | 100000 | 500000 | 1000000 | 5000000 | 10000000
astar | 0.88861 | 0.9184 | 0.92418 | 0.93014 | 0.93469 | 0.9366 | 0.94122 | 0.94548 | 0.94696 | 0.9474 | 0.9493 | 0.94957 | 0.94988 | 0.94997 | 0.95037 | 0.95076
bzip2 | 0.88546 | 0.92197 | 0.93123 | 0.93939 | 0.94211 | 0.94538 | 0.94228 | 0.94875 | 0.94683 | 0.94667 | 0.94621 | 0.94851 | 0.94722 | 0.94682 | 0.9519 | 0.95613
gcc | 0.87417 | 0.9185 | 0.92824 | 0.93678 | 0.94187 | 0.94367 | 0.94715 | 0.94945 | 0.94995 | 0.95014 | 0.95098 | 0.95088 | 0.95104 | 0.95132 | 0.95201 | 0.95314
gobmk | 0.87742 | 0.91306 | 0.92191 | 0.93125 | 0.93691 | 0.93933 | 0.94453 | 0.94812 | 0.94882 | 0.94937 | 0.9503 | 0.95047 | 0.95086 | 0.9509 | 0.95161 | 0.95178
h264ref | 0.88621 | 0.92505 | 0.93416 | 0.94114 | 0.94473 | 0.94574 | 0.948 | 0.94927 | 0.94959 | 0.94968 | 0.94996 | 0.95022 | 0.95021 | 0.95039 | 0.95144 | 0.95175
hmmer | 0.84288 | 0.91178 | 0.9266 | 0.93642 | 0.94132 | 0.94307 | 0.94676 | 0.94862 | 0.94912 | 0.94932 | 0.94988 | 0.94994 | 0.95002 | 0.95018 | 0.95214 | 0.9526
mcf | 1.0051 | 1.0064 | 1.0066 | 1.0066 | 1.0066 | 1.0067 | 1.0067 | 1.0067 | 1.0067 | 1.0067 | 1.0066 | 1.0065 | 1.0063 | 1.0057 | 1.0022 | 1.0014
omnetpp | 0.85591 | 0.90817 | 0.91816 | 0.92944 | 0.93792 | 0.93981 | 0.9433 | 0.9476 | 0.94824 | 0.94878 | 0.9494 | 0.94837 | 0.9494 | 0.94944 | 0.95119 | 0.95151
sjeng | 0.86965 | 0.91434 | 0.9238 | 0.93301 | 0.93906 | 0.94123 | 0.94614 | 0.94936 | 0.95031 | 0.95074 | 0.9519 | 0.95208 | 0.95274 | 0.9529 | 0.95333 | 0.95465
average | 0.88726 | 0.92641 | 0.93498 | 0.94269 | 0.94725 | 0.94906 | 0.95178 | 0.95482 | 0.95517 | 0.95542 | 0.95606 | 0.95629 | 0.95641 | 0.9564 | 0.95735 | 0.95819
Composite Cores
( Quantum Length = 1000 )
Switching overheads negligible until ~1000 instructions

## Slide 20: Fine-Grained vs. Coarse-Grained
Little uEngine’s average power 8% higher
  Due to shared hardware structures
Fine-Grained can map 41% more instructions to the Little uEngine over Coarse-Grained.
Results in overall 27% decrease in average power over Coarse-Grained

## Slide 21: Decision Techniques
Oracle
  Knows both uEngine’s performance for all quantums
Perfect Past
  Knows both uEngine’s past performance perfectly
Model
  Knows only active uEngine’s past, models inactive uEngine using default weights
  All models target 95% of the all Big uEngine’s performance

## Slide 22: Little Engine Utilization
Chart: Dynamic Instructions On Little
| Astar | Bzip2 | Gcc | GoBmk | H264ref | Hmmer | Mcf | OmnetPP | Sjeng | Average
Oracle | 0.58881 | 0.20243 | 0.32821 | 0.40148 | 0.13183 | 0.15401 | 0.97587 | 0.22701 | 0.32032 | 0.37
Perfect Past | 0.39875 | 0.14035 | 0.22761 | 0.28141 | 0.10319 | 0.11015 | 0.9745 | 0.14341 | 0.22058 | 0.28888
Model | 0.2768 | 0.10529 | 0.21771 | 0.25828 | 0.084165 | 0.10445 | 0.7374 | 0.16266 | 0.23924 | 0.24289
High utilization for memory bound application
Issue width dominates computation bound
Maps 25% of the dynamic instructions
onto the Little uEngine

## Slide 23: Energy Savings
Includes the overhead of shared hardware structures
Chart: Energy Savings Relative to Big
| Astar | Bzip2 | Gcc | GoBmk | H264ref | Hmmer | Mcf | OmnetPP | Sjeng | Average
Oracle | 0.45175 | 0.15889 | 0.25556 | 0.30584 | 0.13221 | 0.14666 | 0.70904 | 0.1898 | 0.2516 | 0.28904
Perfect Past | 0.32523 | 0.14783 | 0.20737 | 0.23289 | 0.12473 | 0.1246 | 0.70777 | 0.13942 | 0.19578 | 0.24507
Model | 0.1997 | 0.11073 | 0.16116 | 0.18735 | 0.080564 | 0.09599 | 0.46273 | 0.12437 | 0.17407 | 0.17741
18% reduction in energy consumption

## Slide 24: User-Configured Performance
Chart: 
| 1% | 5% | 10% | 20% | 1% | 5% | 10% | 20% | 1% | 5% | 10% | 20% | Utilization | Overall Performance | Energy Savings
 | 0.069335 | 0.23826 | 0.45206 | 0.57706 | 0.99157 | 0.95432 | 0.91519 | 0.83 | 0.043071 | 0.18424 | 0.34918 | 0.44289
1% performance loss yields 4% energy savings
20% performance loss yields 44% energy savings

## Slide 25: More Details in the Paper
Estimated uEngine area overheads
uEngine model accuracy
Switching timing diagram
Hardware sharing overheads analysis

## Slide 26: Conclusions
Even high performance applications experience fine-grained phases of low throughput
  Map those to a more efficient core
Composite Cores allows
  Fine-grained migration between cores
  Low overhead switching
18% energy savings by mapping 25% of the instructions to Little uEngine with a 5% performance loss
Questions?

## Slide 27: Composite Cores: Pushing Heterogeneity into a Core
Andrew Lukefahr, Shruti Padmanabha, Reetuparna Das, Faissal M. Sleiman, Ronald Dreslinski, Thomas F. Wenisch, and Scott Mahlke
University of Michigan
Micro 45
May 8th 2012

## Slide 28: Back Up

## Slide 29: The DVFS Question
Lower voltage is useful when:
  L2 Miss (stalled on commit)
Little uArch is useful when:
  Stalled on L2 Miss (stalled at issue)
  Frequent branch mispredicts (shorter pipeline)
  Dependent Computation
http://www.arm.com/files/downloads/big_LITTLE_Final_Final.pdf

## Slide 30: Sharing Overheads
Chart: Average Power Relative to the Big Core
| astar | bzip2 | gcc | gobmk | h264ref | hmmer | mcf | omnetpp | sjeng | average
Big uEngine | 1.0008 | 1.0008 | 1.0008 | 1.0008 | 1.0007 | 1.0007 | 1.0014 | 1.0008 | 1.0008 | 1.0008
Little Core | 0.21407 | 0.21419 | 0.23935 | 0.24355 | 0.2158 | 0.20232 | 0.20266 | 0.24154 | 0.23745 | 0.22344
Little uEngine | 0.28815 | 0.26908 | 0.33256 | 0.31536 | 0.30686 | 0.29082 | 0.22497 | 0.34609 | 0.32891 | 0.30031

## Slide 31: Performance
5% performance loss
Chart: Performance Relative to Big
| Astar | Bzip2 | Gcc | GoBmk | H264ref | Hmmer | Mcf | OmnetPP | Sjeng | Average
Oracle | 0.95 | 0.95 | 0.95 | 0.95 | 0.95 | 0.95 | 1.0065 | 0.95 | 0.95 | 0.95628
Perfect Past | 0.95224 | 0.94717 | 0.95156 | 0.95309 | 0.95151 | 0.9514 | 1.0021 | 0.95296 | 0.95318 | 0.95724
Model | 0.96355 | 0.95471 | 0.94963 | 0.95156 | 0.95393 | 0.95192 | 1.0184 | 0.9445 | 0.94684 | 0.95945

## Slide 32: Model Accuracy
Chart: Percent Deviation From Actual
| -1 | -0.95 | -0.9 | -0.85 | -0.8 | -0.75 | -0.7 | -0.65 | -0.6 | -0.55000000000000004 | -0.5 | -0.45 | -0.4 | -0.35 | -0.3 | -0.25 | -0.2 | -0.15 | -0.1 | -0.05 | 0 | 0.05 | 0.1 | 0.15 | 0.2 | 0.25 | 0.3 | 0.35 | 0.4 | 0.45 | 0.5 | 0.55000000000000004 | 0.6 | 0.65 | 0.7 | 0.75 | 0.8 | 0.85 | 0.9 | 0.95 | 1
Model | 0 | 1.128e-07 | 1.128e-07 | 2.2559e-07 | 6.5019e-07 | 4.5118e-07 | 1.1842e-05 | 0.00030116 | 0.0010712 | 0.00017021 | 9.7734e-05 | 0.0008432 | 0.0013826 | 0.001958 | 0.0023803 | 0.0091215 | 0.029269 | 0.036859 | 0.06545 | 0.15368 | 0.24068 | 0.23303 | 0.12401 | 0.052693 | 0.022247 | 0.010909 | 0.0052965 | 0.0022957 | 0.0013303 | 0.00088223 | 0.00067484 | 0.00060925 | 0.00050714 | 0.00031556 | 0.00015015 | 8.7509e-05 | 5.6823e-05 | 4.3853e-05 | 0.0012625 | 7.369e-05 | 0.00025048
Average Performance | 0 | 0 | 1.0977e-05 | 0.00036656 | 0.0014208 | 0.00048464 | 0.00052722 | 0.00076814 | 0.002013 | 0.0034415 | 0.012619 | 0.011241 | 0.029392 | 0.043355 | 0.029134 | 0.026304 | 0.031525 | 0.039821 | 0.048991 | 0.057399 | 0.063933 | 0.067152 | 0.067073 | 0.063836 | 0.056926 | 0.044224 | 0.040194 | 0.02662 | 0.037198 | 0.018574 | 0.03904 | 0.011121 | 0.0077436 | 0.0074003 | 0.0046185 | 0.0088418 | 0.00872 | 0.0051136 | 0.0035048 | 0.0029603 | 0.076392
Chart: Percent Deviation From Actual
| -1 | -0.95 | -0.9 | -0.85 | -0.8 | -0.75 | -0.7 | -0.65 | -0.6 | -0.55000000000000004 | -0.5 | -0.45 | -0.4 | -0.35 | -0.3 | -0.25 | -0.2 | -0.15 | -0.1 | -0.05 | 0 | 0.05 | 0.1 | 0.15 | 0.2 | 0.25 | 0.3 | 0.35 | 0.4 | 0.45 | 0.5 | 0.55000000000000004 | 0.6 | 0.65 | 0.7 | 0.75 | 0.8 | 0.85 | 0.9 | 0.95 | 1
Model | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 4.3556e-07 | 7.8089e-06 | 1.3789e-06 | 1.4071e-05 | 0.00013162 | 0.00063349 | 0.0018388 | 0.0032769 | 0.0075888 | 0.078182 | 0.13912 | 0.30619 | 0.33153 | 0.094984 | 0.019786 | 0.005846 | 0.0028187 | 0.00205 | 0.0021249 | 0.0012185 | 0.00057795 | 0.00026751 | 0.0004263 | 0.00075269 | 0.00010828 | 6.2124e-05 | 4.5879e-05 | 5.006e-05 | 4.7032e-05 | 4.717e-05 | 4.5995e-05 | 0.00022263
Average Performance | 0 | 3.0111e-07 | 7.3233e-06 | 0.00016314 | 0.0006246 | 0.0011653 | 0.00099138 | 0.0015731 | 0.0011563 | 0.001007 | 0.0026686 | 0.0041594 | 0.0053429 | 0.0096571 | 0.02173 | 0.025137 | 0.027688 | 0.042311 | 0.067196 | 0.088267 | 0.098053 | 0.10832 | 0.11292 | 0.1133 | 0.081337 | 0.039042 | 0.03526 | 0.044151 | 0.035329 | 0.0041435 | 0.0025092 | 0.001204 | 0.0016707 | 0.000899 | 0.001076 | 0.0001031 | 0.0001003 | 0.00010882 | 0.0011571 | 3.7203e-05 | 0.018431
Little -> Big
Big -> Little

## Slide 33: Regression Coefficients
Chart: Relative Coefficient Magnatude
| Little -> Big | Big -> Little
Constant | 0.46077 | 0.57053
Active uEngine Cycles | 0.17315 | 0.14912
MLP | 0.14085 | 0.032709
L2 Hit | 0.10366 | 0.15246
ILP | 0.053688 | 0.031156
Branch Mispredicts | 0.053305 | 0.02632
L2 Miss | 0.014582 | 0.037702

## Slide 34: Different Than Kumar et al.
Kumar et al. | Composite Cores
Coarse-grained switching OS Managed | Fine-grain switching Hardware Managed
Minimal shared state (L2’s) | Maximizes shared state (L2’s, L1’s, Branch Predictor, TLBs)
Requires sampling | On-the-fly prediction
6 Wide O3 vs. 8 Wide O3 Has InOrder, but never uses it! | 3 Wide O3 vs. 2 Wide InOrder
Coarse-grained vs. fine-grained

## Slide 35: Register File Transfer
RAT
Num
-
Registers
Num
Value
Registers
Num
Value
Commit
3 stage pipeline
  Map to physical register in RAT
  Read physical register
  Write to new register file
If commit updates, repeat
Notes: 50 mWatt average power
10 mWatt average power

## Slide 36: uEngine Model
Linear model:
  : Average uEngine performance
  : Performance counter value
  Weight of performance counter
Different weights for big and little uEngine models
Fixed vs. per-application weights?
  Default weights, fixed at design time
  Per-application weights