## Slide 1: Libra:Tailoring SIMD Execution using Heterogeneous Hardware and Dynamic Configurability
Yongjun Park1, Jason Jong Kyu Park1 , Hyunchul Park2,
and Scott Mahlke1
December 3, 2012
1University of Michigan, Ann Arbor
2Programming Systems Lab, Intel Labs, Santa Clara, CA

## Slide 2: Convergence of Functionalities
Convergence of functionalities demands a flexible solution due to the design cost and programmability
Anatomy of an iPhone4
4G Wireless
Navigation
Audio
Video
3D
Flexible
Accelerator!

## Slide 3: Current Mobile Solutions & Challenges
Mixture of ILP/DLP
legacy workloads
media processing
web browsing
scientific computing
wireless communication
Image processing
Good for ILP
Good for DLP
1.6 GHz ARM Cortex-A9
ULP GeForce
1.7 GHz Krait
Adreno 320
1.6 GHz ARM Cortex-A9
ARM Mali-400 MP4
ILP-based
DLP-based
Goal: Design of a unified accelerator with:
1. Scalability
2. Flexible execution support
3. Energy efficiency

## Slide 4: Traditional Homogeneous SIMD
4
Standard high performance machine for embedded systems
  Industry: IBM Cell, ARM NEON, Intel MIC, etc.
  Research: SODA, AnySp, etc.
Advantage
  High throughput
  Low fetch-decode overhead
  Easy to scale
Disadvantage
  Hard to realize high resource utilization
Example SIMD machine: 100 MOps /mW
Advanced goal: map broader range of applications into SIMD!

## Slide 5: Exploration of Low Resource Utilization
AAC decoder
High execution ratio on high data-parallel loops (~80%)
Traditional wide SIMD accelerator is frequently over-designed
  The performance is limited by the non-high-DLP loops
Loop Execution Time Breakdown
@ 1-issue in-order core
Input
for ( …… ) {
}
output
for ( …… ) {
}
Huffman decoding
Inverse
Quantization
IMDCT
Application
Acyclic
Loop
Non-DLP
DLP
Low-DLP
High-DLP
Chart: Execution time ratio
| Vision | Media | Game Physics | Avg
non-DLP | 0.12354 | 0.15325 | 0.076667 | 0.11162
low-DLP | 0.037296 | 0.28972 | 0 | 0.074555
high-DLP | 0.83916 | 0.55703 | 0.92333 | 0.81383
Chart: Execution time ratio
| Vision | Media | Game Physics | Avg
non-DLP | 0.12354 | 0.15325 | 0.076667 | 0.11162
low-DLP | 0.037296 | 0.28972 | 0 | 0.074555
high-DLP | 0.05 | 0.05 | 0.05 | 0.05
Execution Time Breakdown
@ 1-issue in-order core

## Slide 6: Additional Flexibility on SIMD
SIMD
Control
RF
RF
FU
FU
Distributed VLIW
Control
RF
RF
FU
FU
Control
  DLP loop
  Non-DLP loop
  Program flow
  Non-DLP loop

## Slide 7: Additional Flexibility on SIMD
8
9
10
11
12
13
14
15
1
2
3
4
5
6
7
0
Libra
8
9
10
11
12
13
14
15
Each logical lane has own ILP capability
  The ILP capability is decided based on SIMD capability
  Total degree of parallelism is consistent
All resources are utilized
for ( …… ) {
}
1
2
3
4
5
6
7
0
Traditional SIMD
1
2
4
8
DLP = 1
ILP = 1
Total: 1
DLP = 1
ILP = 16
Total = 16
16
DLP = 2
ILP = 1
Total: 2
DLP = 2
ILP = 8
Total = 16
DLP = 4
ILP = 1
Total: 4
DLP = 4
ILP = 4
Total = 16
DLP = 8
ILP = 1
Total: 8
DLP = 8
ILP = 2
Total = 16
DLP = 16
ILP = 1
Total: 16
DLP = 16
ILP = 1
Total = 16
Full DLP mode
Full ILP mode
Hybrid mode

## Slide 8: Looks Good, but Too Expensive!
Control
RF
RF
FU
FU
Control
Control
RF
RF
FU
FU
Control
Control
RF
RF
FU
FU
Control
Control
RF
RF
FU
FU
Control
Notes: However, the addition of whole interconnects and control units are too expensive!

## Slide 9: Opportunity: Resource Utilization
Resource over-provision: Lane uniformity incurs inefficiency
  Each SIMD lane provides the same functionalities
  Only 32% (memory) and 16% (multiplication) of total dynamic instructions
  More complex design, more static power consumption
High variation in the resource requirements of loops
  Simple sharing leads to performance degradation
Chart: Memory ratio
Loop distribution over static ratio of multiply and memory instructions
for ( …… ) {
}
Small fraction of mul/mem instructions

## Slide 10: Adapting Heterogeneity (Homogeneous SIMD)
High DLP, 1 Multiplication
SIMD Lane
Cycle
0
1
3
2
ADD
ADD
ADD
Mul
4-way SIMD w/ 4 multipliers
Lane 0
Lane 1
Lane 2
Lane 3
A0
A0
A0
A0
A1
A1
A1
A1
A2
A2
A2
A2
M3
M3
M3
M3
IPC = 4
Notes: The loop is divided by 4 and each lane can execute each of them

## Slide 11: Adapting Heterogeneity (Heterogeneous SIMD)
High DLP, 1 Multiplication
SIMD Lane
Cycle
4-way SIMD w/ 1 multiplier
Lane 0
Lane 1
Lane 2
Lane 3
A0
A0
A0
A0
A1
A1
A1
A1
A2
A2
A2
A2
M3
M3
M3
M3
M3
M3
M3
IPC = 2.29
Stall!!
Notes: However, when only lane 3 is supporting multiplication, severe performance overhead incurs b/c the remaining lanes are idle
When lane 3 executes multiplications of all lanes.

## Slide 12: Adapting Heterogeneity (Heterogeneous SIMD + Flexibility)
Logical lane 0
High DLP, 1 Multiplication
SIMD Lane
Cycle
4-way SIMD w/ 1 multiplier
Lane 0
Lane 1
Lane 2
Lane 3
A0
A0
A1
A0
A1
A2
A0
A1
A2
M3
A1
A2
M3
A2
M3
M3
IPC = 4

## Slide 13: Libra: Loop-adaptive SIMD Accelerator
Region-adaptive execution strategy customization
Key insights
  Heterogeneous lane structure: less power/area
  Dynamic configurability: change ILP/DLP capability
    # of logical lanes: DLP, size of a logical lane: ILP
High-DLP loops
Low/No-DLP loops
Application
ExOp-intensive loops
Int
Expensive unit
Int
Expensive unit
Int
Expensive unit
Int
Expensive unit
Int
Expensive unit
Int
Expensive unit
Int
Expensive unit
Int
Expensive unit
Traditional SIMD
Heterogeneous SIMD
0
1
2
3
4
5
6
7
0
1
2
3
0
1

## Slide 14: Libra Hardware Implementation
Fully distributed nature including FUs, register files, and interconnections
No dynamic routing logic: all communications statically generated
Intra-group Configurable Interconnect
Inter-group Configurable Interconnect
Integer ALUs in all 4 FUs
One multiplier and memory unit per PE group
Dense 4x8 full crossbar
between FUs w/o writback
Each FU is only connected to the corresponding neighbors in adjacent PE groups

## Slide 15: Resource Sharing @ Full DLP Mode
Logical Lane 0
Logical Lane 1
2-wide transfer
& data bypass
A0
B0
C0
D0
A1
B1
C1
D1
Simple hardware sharing
Execute 1 cycle difference for
avoiding resource contention

## Slide 16: Compilation Overview
Compiler Front-end
Classifying the loop
Resource allocation
Code Generation
Generic C
program
Hardware
Information
Determine SIMDizability
Set SIMD mode
Set ILP mode
Profile
Information
Modulo
scheduling
List scheduling
w/ multi-threading
Executable

## Slide 17: Experimental Setup
Target applications
  Vision applications: SD-VBS [Venkata, IISWC '09]
  Media benchmark: AAC decoder, H.264 decoder, and 3D rendering
  Game physics benchmarks: line of sight, convolution, and conjugate
Target architecture: SIMD, clustered VLIW, and Libra
  16 ~ 64 heterogeneous/homogeneous resources
IMPACT frontend compiler + cycle-accurate simulator
Power measurement
  IBM SOI 45nm technology @ 500MHz/0.81V

## Slide 18: Performance with Heterogeneous Hardware
Performance @ 32 heterogeneous datapath
Libra is 2.04x/1.38x faster than heterogeneous SIMD/VLIW
Chart: Normalized Execution Time
| SIMD | VLIW | Libra | SIMD | VLIW | Libra | SIMD | VLIW | Libra | SIMD | VLIW | Libra | SIMD | VLIW | Libra | SIMD | VLIW | Libra | SIMD | VLIW | Libra | SIMD | VLIW | Libra | SIMD | VLIW | Libra | SIMD | VLIW | Libra | SIMD | VLIW | Libra | disparity | local | stitch | svm | tracking | AAC | 3D | H.264 | lineOfS | Conv | Conj | Vision | Media | Game Physics
SIMDizable | 0.061469 | 0.076222 | 0.046118 | 0.066354 | 0.12833 | 0.046696 | 0.16428 | 0.20813 | 0.1374 | 0.060201 | 0.12162 | 0.049224 | 0.062301 | 0.087571 | 0.058889 | 0.048347 | 0.072672 | 0.046633 | 0.16253 | 0.080833 | 0.062518 | 0.1559 | 0.10003 | 0.10519 | 0.044061 | 0.074172 | 0.04406 | 0.070047 | 0.067321 | 0.04586 | 0.061404 | 0.10152 | 0.047994
SWPable (non-SIMDizable) | 0.14 | 0.014913 | 0.021989 | 0.019233 | 0.0020539 | 0.0029259 | 0.37 | 0.12091 | 0.12803 | 0 | 0 | 0 | 0.04 | 0.012215 | 0.012215 | 0.33375 | 0.14199 | 0.12739 | 0.11555 | 0.010622 | 0.016877 | 0.024383 | 0.0052667 | 0.0089576 | 0.21601 | 0.072038 | 0.072034 | 0 | 0 | 0 | 0 | 0 | 0
Chart: 
| SIMD | VLIW | Libra | Avg
 | 0.20144 | 0.13622 | 0.098273
Notes: Same resources.
Normalized execution time to 1issue cores, lower is better.
Yellow bar : execution time at non DLP loops
Blue bar: execution time at DLP loops
Libra beat SIMD the benchmarks with low DLP loops
Libra also beat the SIMD the benchmarks with high DLP loops for heterogeneity.
Libra is better than VLIW b/c the scheduling large unrolled loop in the wide resource has high difficulties
Libra is scalable

## Slide 19: Scalability with Heterogeneous Hardware
Chart: Normalized Performance
| 16 | 32 | 64 | 16 | 32 | 64 | 16 | 32 | 64 | 16 | 32 | 64 | Vision | Media | Game | Average
SIMD | 5.4748 | 8.9811 | 14.2652 | 3.571 | 3.92 | 4.0876 | 5.9826 | 10.7087 | 19.1322 | 5.0094 | 7.8699 | 12.495
VLIW | 5.6157 | 7.9851 | 8.3911 | 5.0477 | 8.3757 | 8.8704 | 7.3614 | 10.2203 | 11.7849 | 6.0082 | 8.8604 | 9.6821
Libra | 8.5948 | 14.5963 | 23.2419 | 5.8512 | 9.034 | 11.8468 | 8.8801 | 15.8876 | 27.7433 | 7.7754 | 13.1726 | 20.944
Libra is scalable when having enough total ILP/DLP parallelism

## Slide 20: Homogeneous SIMD vs. Heterogeneous Libra
Performance of Libra is better than SIMD
Energy consumption shows similar trend
  Less expensive functional units can reduce the overall power overheads
  Ex. Total 11% power overheads @ 32 PEs
Chart: # of PEs
| 16 | 32 | 64
Perfomance | 1.2235 | 1.579 | 1.9209
Chart: # of PEs
| 16 | 32 | 64
Power efficiency | 1.016 | 0.70752 | 0.56098
Chart: Relative power
| homogeneous SIMD | heterogeneous Libra
FU | 0.41735 | 0.29766
RF | 0.41527 | 0.40845
Control | 0.15405 | 0.26175
D-mem | 0.013326 | 0.013326
Extra | 0 | 0.13598
(-) FU power saving
(+) Control power
overhead
Power breakdown@32-PE
Performance
Energy consumption

## Slide 21: Mode Selection
All available modes are used for considerable fraction
The mode is selected based on application characteristics
Distribution of loop execution modes
Chart: Execution time ratio
| 16 | 32 | 64 | 16 | 32 | 64 | 16 | 32 | 64 | 16 | 32 | 64 | Vision | Media | Game Physics | Avg
2 | 0.58604 | 0.49503 | 0.40275 | 0.14008 | 0.13534 | 0.071889 | 0.39296 | 0.3805 | 0.36979 | 0.37303 | 0.33696 | 0.28148
4 | 0.069696 | 0.069479 | 0.06913 | 0.14372 | 0.05964 | 0.058811 | 0.45699 | 0.41267 | 0.37515 | 0.22347 | 0.1806 | 0.1677
8 | 0.16234 | 0.070911 | 0.071346 | 0.17579 | 0.17093 | 0.093674 | 0 | 0 | 0 | 0.11271 | 0.080614 | 0.055007
16 | 0.18192 | 0.22196 | 0.30281 | 0.54041 | 0.31806 | 0.2739 | 0.15005 | 0.20683 | 0.25506 | 0.2908 | 0.24895 | 0.27726
32 | 0 | 0.14262 | 0.10029 | 0 | 0.31603 | 0.20309 | 0 | 0 | 0 | 0 | 0.15288 | 0.10113
64 | 0 | 0 | 0.053679 | 0 | 0 | 0.29864 | 0 | 0 | 0 | 0 | 0 | 0.11744
Logical lane size

## Slide 22: Conclusion
Mobile applications consist of loops with wide range of different level of ILP and DLP.
Heterogeneous SIMD lane structure can reduce the power overhead of over-provided resources.
Dynamic configurability enables broader applicability.
Libra outperforms traditional SIMD by 1.58x performance improvement with 29% less energy consumption on 32-PE architectures.

## Slide 23: Questions?
For more information
  http://cccp.eecs.umich.edu