## Slide 1
Unifying Primary Cache, Scratch, and Register File Memories in a Throughput Processor
Mark Gebhart1,2 Stephen W. Keckler1,2 Brucek Khailany2 Ronny Krashinsky2 William J. Dally2,3
1The University of Texas at Austin 2NVIDIA 3Stanford University
Methodology
Generated execution and address traces with Ocelot
Performance and energy estimates come from custom SM trace-based simulator
30 CUDA benchmarks drawn from CUDA SDK, Parboil, Rodinia, GPGPU-sim
  22 with limited memory requirements that don’t benefit
  8 that see significant benefits
Motivation
GPUs have thousands of on-chip resident threads
  On-chip storage per thread is very limited
On-chip storage split between register file, scratchpad, and cache
Applications have diverse requirements between these three types of on-chip storage
Efficiently utilizing on-chip storage can improve both performance and energy
Overview
Automated algorithm determines most efficient allocation
Overheads are mitigated by leveraging prior work on register file hierarchy
Traditional Design
Proposed Unified Design
Register File
Shared Memory
Cache
Program A Program B
Register File
Shared Memory
Cache
Register File
Shared Memory
Cache
Performance and energy overheads for benchmarks that do not benefit are less than 1%
Performance improvements up to 71% along with significant energy and DRAM reductions
Results
Allocation Algorithm
SIMT Lanes
SFU
TEX
MEM
ALU
Register File Hierarchy
Main Register File
Shared Memory Cache
Streaming Processor (SM)
Background
32 SMs per chip
Each SM contains:
  32 SIMT lanes
  Register file hierarchy
  256KB main register file
  64KB shared memory
  64KB primary data cache
MRF
(4 banks)
MEM
Unit
Shared Memory / Cache Crossbar
Shared Memory (32 banks)
Cache (32 banks)
Cache Tags
MRF
(4 banks)
MEM
Unit
MRF
(4 banks)
MEM
Unit
Unified
(4 banks)
MEM
Unit
Shared Memory / Cache Crossbar
Cache Tags
Unified
(4 banks)
MEM
Unit
Unified
(4 banks)
MEM
Unit
Microarchitecture
Total of 96 banks in baseline design
Unified design has only 32 banks
Challenges:
  Bank access energy
  Bank conflicts
Baseline
Unified
Related Work
Allocate enough registers to eliminate spills
Programmer dictates shared memory blocking
Maximize thread count subject to register and shared requirements
Devote remaining storage to cache
Fermi has a limited form of flexibility between shared memory and cache, programmer chooses either:
  16KB shared memory and 48KB cache
  48KB shared memory and 16KB cache