## Slide 1: Unifying Primary Cache, Scratch, and Register File Memories in a Throughput Processor
Mark Gebhart1,2 Stephen W. Keckler1,2
Brucek Khailany2 Ronny Krashinsky2
William J. Dally2,3
1The University of Texas at Austin
2NVIDIA
3Stanford University

## Slide 2: Motivation
GPUs have thousands of on-chip resident threads
  On-chip storage per thread is very limited
On-chip storage split between register file, scratchpad, and cache
Applications have diverse requirements between these three types of on-chip storage
Efficiently utilizing on-chip storage can improve both performance and energy

## Slide 3: Overview
Automated algorithm determines most efficient allocation
Overheads are mitigated by leveraging prior work on register file hierarchy
Traditional Design
Proposed Unified Design
Register File
Shared Memory
Cache
Program A Program B
Register File
Shared Memory
Cache
Register File
Shared Memory
Cache

## Slide 4: Contemporary GPUs
Large number of SMs per chip
High bandwidth memory system
Each SM contains:
  Parallel SIMT lanes
  High capacity register file
  Programmer controlled shared memory
  Primary data cache
  Coarse-grain configurability between shared memory and cache

## Slide 5: Baseline Streaming Processor
Each SM contains:
  32 SIMT lanes
  256KB main register file
  64KB shared memory
  64KB primary data cache
  Register file hierarchy
SIMT Lanes
SFU
TEX
MEM
ALU
Register File Hierarchy
Main Register File
Shared Memory Cache
Streaming Multiprocessor (SM)
Register File Hierarchy
L0 RF
L1 RF
Main
Register File
ALUs
[Gebhart, MICRO 2011]

## Slide 6: Outline
Motivation
GPU background
Unified GPU on-chip storage
  Sensitivity study
  Microarchitecture
  Results
Conclusions

## Slide 7: Sensitivity Study
Evaluate the performance impact of memory capacity of three structures:
  Larger Register file
    Increase the number of registers per threads
    Increase the number of concurrent threads
  Larger Shared Memory
    Refactor code to use more shared memory per thread
    Increase the number of concurrent threads
  Larger Cache
    Better exploit locality

## Slide 8: Register File Sensitivity Study
Chart: DGEMM
| 18 | 36 | 54 | 72 | 32 | 64 | 96 | 128 | 40 | 80 | 120 | 160 | 64 | 128 | 192 | 256
18 | 0.013377 | 0.013498 | 0.013487 | 0.01348
32 | 0.35906 | 0.45694 | 0.46911 | 0.54986
40 | 0.57489 | 0.69183 | 0.6849 | 0.75174
64 | 0.75909 | 0.92148 | 0.9146 | 1
256, 512, 768, 1024 threads per SM

## Slide 9: Register File Sensitivity Study

## Slide 10: Shared Memory Sensitivity Study
Needle
256, 512, 768, 1024 threads per SM

## Slide 11: Shared Memory Sensitivity Study
Needle
PCR
STO
LU

## Slide 12: Cache Capacity Sensitivity Study

## Slide 13: Cache Capacity Sensitivity Study

## Slide 14: Workload Characterization Summary
Wide range of ideal capacities for each different type of memory
Performance is most sensitive to excessive register spills
Some applications see significant benefits from large caches
  Fewer DRAM accesses both improves performance and reduces energy

## Slide 15: Proposed Design
Challenges:
  Performance overhead of bank conflicts
  Energy overhead of bank access
  Allocation decisions
Traditional Design
Proposed Unified Design
Register File
Shared Memory
Cache
Program A Program B
Register File
Shared Memory
Cache
Register File
Shared Memory
Cache

## Slide 16: Baseline Microarchitecture
SM is composed of 8 clusters
Total of 96 banks
  32 register file banks
  32 L1 cache banks
  32 shared memory banks

## Slide 17: Unified Microarchitecture
Total of 32 unified storage banks
  Increase in bank conflicts
  Increase in bank access energy

## Slide 18: Allocation Algorithm
Allocate enough registers to eliminate spills
Programmer dictates shared memory blocking
Maximize thread count subject to register and shared requirements
Devote remaining storage to cache
Registers per thread
Bytes of shared memory per thread
Runtime Scheduler
Compiler
Programmer
Cache capacity
Number of threads to run

## Slide 19: Methodology
Generated execution and address traces with Ocelot
Performance and energy estimates come from custom SM trace-based simulator
30 CUDA benchmarks drawn from CUDA SDK, Parboil, Rodinia, GPGPU-sim
  22 with limited memory requirements that don’t benefit
  8 that see significant benefits

## Slide 20: Overheads
For applications that don’t benefit
  <1% performance overhead
  <1% energy overhead

## Slide 21: Allocation Decisions
Different allocation decisions are made across benchmarks
  Register file usage ranges from 50 to 250KB
  Cache usage ranges from 50 to 300KB
  Needle requires a large amount of shared memory

## Slide 22: Results
Performance improvements range from 5—71%
Energy and DRAM reductions up to 33%
Leads to substantial efficiency improvements

## Slide 23: Comparison with Limited Flexibility
Unified design outperforms limited flexibility design that only unifies shared memory and cache
  mummergpu underperforms with unified design due to interactions with scheduler

## Slide 24: Summary
Applications have diverse needs from on-chip storage
Unified memory presents minimal overheads
  Register file hierarchy mitigates bank conflicts
Moderate performance gains for large number of applications
Enables a more flexible system